## Slide 1: Working with the Jackals
Aswin Jayaprakash, Prithvi Kambhampati, and James Radwill

## Slide 2: Goals of the Project
Finally work with real robots!
Create a URDF Model of the SICK LIDAR.
Integrate the LIDAR and publish the data in an appropriate frame.
Autonomously navigate and map a floor of the EERC.

## Slide 3: LIDAR URDF
2 links
  The bracket (CAD)
  The LIDAR (a box)
2 joints
  The bracket to the robot
  The LIDAR to the bracket
Defined mass and inertia parameters

## Slide 4: LIDAR Inertia Parameters
Assumed a solid even mass and calculated ixx, iyy, and izz as follows.
wikipedia.com

## Slide 5: Integrating LIDAR
Used the sicktoolbox_wrapper
  Set the port, baud, and launch.
By naming the body of the LIDAR “laser” and keeping the default frame for the SICK, we were able to avoid publishing a transform.

## Slide 6: Navigation
Used a modified version of an algorithm from lab 2.
  Originally developed by Derek Chopp, Akhil Kurup, and James Radwill
Bags the /tf and /scan topics
Stops after 10 mins
  Sufficient for most cases
Doesn’t do well with chairs and tables.
Also included a second launch file and python script that does playback and mapping. (To be run offline)

## Slide 7: The Map

## Slide 8: Problems Encountered
Working outside of WiFi
  Don’t set the ROS_IP param and use screen command
Mapping didn’t do well in corners
  Had to increase the update rate params for gmapping

## Slide 9: Contribution
Aswin – Developed and tested the bagging and mapping portion of the project.
Prithvi – Incorporated and modified the navigation script.
James – Developed the URDF model and integrated the SICK.
Original credit for the navigation algorithm goes to Derek, Akhil, and James.
And of course, a lot of de-bugging and troubleshooting was done by all.

## Slide 10: Questions?